## Slide 2: Neutrino activities at CERN
M. Calviani (CERN)
With contributions from M. Nessi, R. Steerenberg, I. Efthymiopoulos, A. Ferrari, P. Sala, V. Venturi, A. Perillo-Marcone, C. Strabel, H. Vincke, J. Osborne, M. Battistin, S. Girod, K. Kershaw, L. Faisandel, M. Archambault
International Workshop of Next Generation Nucleon Decay and Neutrino Detectors (NNN13)

## Slide 3: Outline of the talk
Recent neutrino beams at CERN
  CNGS experience
CERN Neutrino Project and perspectives
  Detectors R&D and design for a neutrino beam
EU-funded studies
  LAGUNA-LBNO and HP-PS

## Slide 4: Recent neutrino beams at CERN

## Slide 5: CERN Neutrinos to Gran Sasso (CNGS) experience
Long-baseline (730 km) n beam designed for oscillation studies with nt appearance
  2 optimised detectors at LNGS:
    OPERA (1.2 kt)
    ICARUS (0.6 kt)
3.5 GeV (threshold for t production)
Energy spectrum of nm well matched to R~stCC/En2 at ~17 GeV to maximize signal rate
2006 -2012

## Slide 6
400 GeV primary beam
~510 kW (100% df)
Intensity per extraction = 2.4*1013 p
~4.5*1019 POT/y (max)

## Slide 7
Magnetic horns
CNGS target

## Slide 8: CNGS status
CNGS program has completed at the end of 2012, cumulating 1.85*1020 POT
  Lots of operational experience in running a high power target facility
OPERA successfully detected 3 nt, with further analysis ongoing
  http://arxiv.org/pdf/1308.2553v1.pdf
ICARUS 600 ton LAr fully operational and exploited for physics
  http://arxiv.org/abs/1209.0122, etc.
Area up to target presently going to be reused for a proof-of-principle experiment (AWAKE)
See D. Gibin presentation, this workshop
See N. Naganawa presentation, this workshop

## Slide 9: CERN Neutrino Project

## Slide 10: CERN Neutrino Project
R. Heuer (CERN DG), P5 meeting, 2nd November 2013 (link)

## Slide 11: Feedbacks from committees
From ESG (link):
  CERN should develop a neutrino program to pave the way for a substantial European role in future long-baseline experiments
  Europe should explore the possibility of major participation in leading long-baseline neutrino projects in the US and Japan
From SPSC108:
  […] it is important to strenghten the neutrino activities at CERN
  […] The SPSC considers that a new short baseline neutrino beam at the SPS could be an adequate facility to foster this focus in the near future […]

## Slide 12
Neutrino detectors R&D
Logistics & test beam infrastructure
Investigate new programs
(m storage ring, beta beams)
Design (and implement) a neutrino beam at CERN
EU participation in a High Intensity Facility (detectors, beam, infrastructure)
CERN Neutrino Platform
PHYSICS
Approved
Approved
PL: M. Nessi (CERN)

## Slide 13: Neutrino detectors R&D
WA104 (SPSC-P-347)
  rebuild ICARUS T600 at CERN
  R&D on new large LAr TPC (i.e. event reconstruction)
  R&D on an AIR core muon detector (NESSiE) or eventually integrated a solenoid in the main TPC
  Sterile neutrino physics w/ neutrino beam, cross-section measurement, large event samples, etc.
WA105 (SPSC-EOI-007)
  R&D on a 2 phases large LAr TPC prototype
  LAGUNA-PROTO construction
  Events reconstruction
MIND: R&D on muon tracking detectors
2014 -2018

## Slide 14: nmne “anomalous” oscillations
Exploring the existance of one or more sterile neutrinos (SPSC-P-347)
μe
μe
1 year nm beam
2 years anti-nm beam
LSND allowed region is fully explored in both cases
Allowed region in a global 3+1 neutrino fit
Giunti et al. 2013
See D. Gibin presentation, this workshop

## Slide 15: Logistics & test beam infrastructure
Extension of the existing North Area experimental facility
  Make use of existing test beam infrastructure
  Charged particle beams, from few GeVs to 20 GeV, and neutrino (if approved)
    n beam at ~6.5 meters below the floor of EHN1
  Cryogenic services
  460 meters from target(s) – no background muons
ICARUS T150, LAGUNA-PROTO, NESSiE, MIND + possible new detectors
2014 -2016

## Slide 16
LAGUNA-PROTO
NESSiE
ICARUS T150
~64 meters
MIND
New detectors?
n + charged beams for all experiments

## Slide 17: CERN Neutrino Facility design study
Primary beam extraction from TT20
Target area
Near detector facility
~460 m from target
Far detector facility
~1600 m from target

## Slide 18
Existing EHN1 buiding
Neutrino target area
EHN1 extension
460 meters

## Slide 19
proposed
proposed
80-90s
2006-2012
CERN’s PS/SPS complex

## Slide 20: Primary proton beam characteristics
Primary beam momentum 100 GeV/c (new extraction line)
Fast extraction: beam excitation via injection kicker in LSS1 and extraction in LSS2
  Novel solution successfully tested for low intensities beams (2012)
~720 kJ/pulse  ~200 kW on target (max)
Beam time structure similar to CNGS
 Up to 4.5x1019 POT/y

## Slide 21: Secondary beam production
Due to the shallow depth of the beam line (~14 meters), a target area approach based on long tunnels (i.e. CNGS, WANF, etc.) is not applicable
A multi-compartment solution similar to T2K/NuMI has been therefore developed, taking into account the specificities of CERN

## Slide 22
Beam line under He, to avoid NOx formation and to reduce air activation
Angle, distance and depth optimised to keep dose rate in EHN1 <1 mSv/h
Target shielding such that dose rate in target building area <15 mSv/h
Air treatment and water recuperation
Civil engineering drillings/soil tests already performed, yielding promising results
Target cavern and hall
Decay pipe
Hadron absorber and m pits

## Slide 23: Secondary beam production
Target area trasveral cross-cut
Hadron absorber / muon pits longitudinal cut

## Slide 24: Secondary beam production
18 m
2.4 m
Integration of target trench, 3x3 m2, matching DP diameters
Preliminary design of the support module, pure vertical movements

## Slide 25: Neutrino beam optimisation
5 GeV pion focusing – central nm energy ~1.8 GeV
Target inside horn, followed by reflector
Perfect focus within 1 rad
Initial configuration
Best configuration
Far detector:
  ~1M nm /y
  ~20k ne /y

## Slide 26: Neutrino beam optimisation
DP radius
150 cm
DP radius
250 cm
e x100
μ
e x100
μ
Baseline DP radius of 150 cm
Effect of radius increase (e.g. to 250 cm):
  Increase in nm rate at low energy (20% at 1 GeV)
  Small increase in total (5-10% integrated)
  Slightly larger increase of intrinsic ne (15%)

## Slide 27: CENF target R&D
100 cm long, 12 mm Ø  challenging design
  ~2 kW dep. power, He-cooled graphite PT2020
Graphite to be maintained around 600-700 K to minimize mechanical properties change due to radiation effects
Baseline fully inserted inside horn
helium is blown into the Be-Be channel and comes back from the C-Be internal channel

## Slide 28
5 graphite fit bars, 20 cm each to compensate for high fragility
He inlet/outlet at plenum
inlet
outlet
Prototype foreseen during 2014
Downstream window

## Slide 29: Target CFD results
VALUE | CFX-Thermal
Temp graphite [K] | 740 – 590
Max temp Be [K] | 545
P inlet [bar]- V outlet [m/s] | 15 80
DP [kPa] | 1.4
DT He [k] | 230
Max He Velocity [m/s] | 100
He flow | 0.4 g/ s
Thermal compressive stress: <2 MPa
Max graph. radial expansion: ~120 mm
Stresses due to pressure on Be structure (@20bar): 25 MPa (max)

## Slide 30: Radioprotection
Radioprotection pivotal aspect for the design of the installation
Additional complication due to the proximity to CERN fence (~70 meters)
Analysis performed:
  Air activation  max annual releases <10 TBq/y
  High energy hadrons and cumulated dose
  Waste zoning
  Prompt dose and soil activation
  Residual dose rates

## Slide 31
Prompt dose in accessible areas during operation <15 mSv/h
Residual dose rate in service pit (above He-vessel), 0.1 – 1 mSv/h
High energy hadron fluence in the target hall is <106 HEH/cm2/y  ok for electronics

## Slide 32
Yearly ambient dose rate at CERN fence is ≤5 mSv/y

## Slide 33: Cooling and ventilation configuration
CENF ventilation design respects ISO17873:2004*
Pressure cascade of multicompartments (from -60 to -220 Pa)
  Flow rate: between 1 and 5 volumes/h
  HEPA filters
  Low humidity control in the service pit
(*) adapted for nuclear instalallation other than nuclear reactors

## Slide 34: Cooling and ventilation configuration

## Slide 35
CV integration inside the target and HS buildings

## Slide 36: Summary
A sound technical design for a new CERN neutrino beamline is being developed
  A special thank to T2K colleagues
Facility designed for a beam power of 200 kW, but the design is scalable for higher power
A design study report will be released during the course of 2014

## Slide 37: EU-funded studies

## Slide 38: LAGUNA-LBNO design study
Design study for the realization of an European LBL experiment with beams from CERN to Pyhäsalmi in the framework of FP7
  Initial beam from SPS(+) 400 GeV/750 kW
  Longer term: LP-SPL to HP-PS 50 GeV/2 MW
Study of primary beam possibilities
Secondary beam, decay volume, dump, etc.
2011 -2014

## Slide 39: Secondary Beam optimisation
Objective is to maximize the n CC rate in the FD location at 2300 km from CERN
  Taking into account both beam operation
Conceptual design of the line based on a CNGS+ configuration

## Slide 40: Civil engineering aspects
Challenges for the design:
  18% slope (CNGS was 5.4%)
  100 m long Fe absorber (m in ND)
  ND (800 m from target) at -180 m depth

## Slide 42
superferric

## Slide 43: Conclusions

## Slide 44: Conclusions
CNGS successfully ended operation at the end of 2012
CERN activities on neutrinos continue with the creation of the CERN Neutrino Project
  For the moment focus on collaborative efforts for neutrino detector R&D and detector tests with charged particle beams
  Completion of the design of a multipurpose neutrino beam line (200 kW)
    Neutrino test beam for detector R&D
    Possible use for physics (final assessment of sterile neutrino issue) & cross-section measurements