## Slide 1: Future Neutrino Beam in J-PARC
Tetsuro Sekiguchi
IPNS, KEK

## Slide 2: Contents
Introduction
Upgrade Plan of J-PARC accelerator
Upgrade Plan of Neutrino Facility
Summary

## Slide 3: J-PARC
Materials and Life Science
Experimental Facility (MLF)
Hadron Experimental Facility
Rapid Cycle Synchrotron (RCS)
(3 GeV synchrotron)
(25 Hz, 1MW)
Linac
(330m)
Main Ring (MR)
(30 GeV synchrotron)
(0.75MW)
500 m
Neutrino Experimental
Facility

## Slide 4: Neutrino Facility
Beam
Dump
Primary
Beam-line
Extraction
Point
Muon
Monitors
110m
280m
295km
To Kamioka
Main
Ring
Target
Horns
P
p
m
n
Decay
Volume
Near Neutrino
Detectors

## Slide 5: Neutrino Beamline
Conventional neutrino beam
  p + C  p+  m+ + nm
Designed for T2K experiment
  High intensity beam
    750kW proton beam (30 GeV, 3.3x1014 protons/pulse)
  Off-axis beam (2~2.5o)
    Narrow band beam ~ 0.6 GeV
      1st oscillation maximum
p+ -> m+ + nm decay
q
Target
Horns
Decay Pipe
SK
Oscillation
Maximum

## Slide 6: Secondary Beamline
a
Target Station (target and horns inside He vessel)
Decay volume
Beam dump

## Slide 7: Target Station
15.0m
10.6m
Baffle
Graphite
Collimator
Horn-1
Horn-2
Horn-3
Beam window
Ti-alloy
DV
collimator
Large flange, sealed with
Al plates, t= 120mm
3 horns / a baffle are placed inside He vessel
Apparatus on the beam-line highly irradiated after beam.
Handled by remote-controlled crane.
Service Pit
OTR
Target
Beam

## Slide 8: Target
Remote maintenance
26mmf x 910mm
Ti-6Al-4V
(0.3mmT)
Graphite
IG-430U
He-gas cooling
DT~200K ~7MPa (Tensile strength 37MPa)
736oC
30GeV-750kW (~20kW heat load)
CFX analyses
9Nm3/min
(v=200m/s)
Conductivity 14020W/mK(rad. damage)

## Slide 9: Magnetic Horns
Aluminum alloy conductor (A6061-T6)
  Double cylinder (inner: t3mm, outer: t10mm)
  Tensile strength: 310MPa  95MPa after 5x108 cycle
  25MPa allowable stress (taking into account corrosion)
  Safety factor ~ 2
320kA pulsed current (rated)
  2.1 T (max.) toroidal field
  2~3ms pulse width
  0.4Hz rep. rate  1 Hz for 750kW
Water cooled
  Total heat load: 25kJ @ 750kW
    15kJ (beam) + 10kJ (Joule)
  Spraying water to inner conductor

## Slide 10: Decay Volume & Beam Dump
Decay Volume
  100m-long
  Water cooled iron walls  4MW
  2~2.5o OA angle for SK and HK
Beam Dump
  Graphite core
  Water cooled  3MW
Designed for multi-MW beam since no access is possible after beam operation due to irradiation

## Slide 11: Operation History
Delivered # of Protons
Protons Per Pulse
1.43x1020pot
until Mar.11,’11
3.01x1020pot
Jun.9,’12
Rep=3.52s
50kW
[6 bunches]
3.2s3.04s
145kW
2.56s
190kW
Mar.8, 2012
Run-1
Run-2
Run-3
2.48s
235kW
Run-4
0
10
20
30
40
x1019
0
20
40
60
80
x1012
100
6.63x1020pot
until May.8,’13
120
50
60
70
2.2x106
4.7x106
7.7x106
1.2x107
Total # of pulses
1.2x1014 ppp: world record of extracted protons/pulse for synchrotron
No replacement of target and horns up to 1.2x107 pulses

## Slide 12: Contents
Introduction
Upgrade Plan of J-PARC accelerator
Upgrade Plan of Neutrino Facility
Summary

## Slide 13: Linac Upgrade
New accelerating structure, ACS, will be installed to increase the extracted beam energy from 181MeV to 400MeV (JFY2013)
Front-end part (IS+RFQ) will be replaced to increase peak current from 30mA to 50mA (JFY2014)
RF antenna
Collab. w/ SNS

## Slide 14: MR Upgrade
Number of protons/pulse is limited by beam loss due to space charge effect
  ~450kW is estimated upper limit with current apparatus.
To achieve 750kW
  Higher beam energy than 30GeV
    Too high power consumption P50GeV=4xP30GeV
  Higher rep. rate than 0.4Hz
    1.3sec cycle with 2.0x1014 protons/pulse
We choose higher rep. rate scenario for 750kW

## Slide 15: MR Upgrade
2kW  3.5kW

## Slide 16: MR Upgrade Timeline
750kW
400kW
300kW
200kW
150kW

## Slide 17: Contents
Introduction
Upgrade Plan of J-PARC accelerator
Upgrade Plan of Neutrino Facility
Summary

## Slide 18: Acceptable Beam Power
Acceptance of each component for high power beam
  Target
    Mechanical: 0.75MW
    Cooling: 0.75MW
  Horn
    Cooling for conductors: 1.85MW
    Cooling for striplines: 0.4MW
    Hydrogen production: 0.3MW
    Power supply: 0.4Hz, 250kA
  He vessel, Decay Volume & Beam Dump
    Cooling: 4MW(HV&DV), 3MW(BD)
  Facility
    Water disposal: 0.5MW
    Radio-active air: 0.5MW

## Slide 19: Hydrogen Production in Horn
H2 production by water radiolysis (2H2O2H2+O2)
  H2 production rate: 40L/day (0.7%/day) @750kW
  H2 must be removed.  H2 recombination (2H2+O22H2O)
Buffer tank
Pump
Suction pump
He vessel
Height
~8m
Service Pit
Machine Room
H2O
He
He gas line
H2
Beam

## Slide 20: Hydrogen Production in Horn
H2 recombination + forced circulation outside He vessel
  H2 density after 1 week 220kW beam
    1.6% near horn, 1.0% in tank
      ~1.5% expected w/o recomb. H2 inside horn not removed.
    Forced circulation inside horn is really necessary.
Buffer tank
Pump
Suction pump
He vessel
Height
~8m
Service Pit
Machine Room
H2O
He
He gas line
H2
Beam
diffusion
H2: 1.6%
O2: 0.7%
H2: 1.0%
O2: 0.03%
Acceptable beam power
~300kW
Catalyst canister
(Catalyst = Alumina pellet with 0.5%Pd )

## Slide 21: Hydrogen Production in Horn
Forced circulation inside horns
  New horns have forced circulation lines
    H2 density will be below 1% even with higher power beam
    New horn will be installed in FY2013
Buffer tank
Pump
Suction pump
He vessel
Height
~8m
Service Pit
Machine Room
H2O
He
He gas line
H2
Beam
Forced circulation
Acceptable beam power should be checked with beam

## Slide 22: Horn Power Supply
New power supply production for 1Hz operation,
  Designed for 320kA operation
  Energy recovery (~50% of stored energy recycled)
  Low input load
    One horn is operated with a power supply
    Low impedance striplines are also developed
Production is on going  Operation from fall in 2014.
PS (K2K)
PS(New)
5.5 kV
4.1 kV
PS(New)
PS (New)
5.8 kV
PS (New)
4.3 kV
5.5 kV
@ 250 kA, 0.4Hz
@ 320 kA, 1Hz

## Slide 23: Disposal of Radio-active Water
Maintenance scenario
  Be7: 53GBq/1020pot  removed by ion-exchanger (99.9%)
  Tritium: 24GBq/1020pot  dilution & disposal
Present capacity
  80 dilution cycles/year (3 working days/cycle)
  Acceptable beam power is ~500kW
Remove
99.9 % of 7Be
80times
/year
Accessible during beam
No access during beam
Regulation
Be7 < 30Bq/cc
H3 < 42Bq/cc

## Slide 24: Disposal of Radio-active Water
Upgrade of water disposal system
  New building for water disposal system is planned.
  240m3 DP tank (320m3 in total)  2MW acceptable
Remove
99.9 % of 7Be
80times
/year
Accessible during beam
No access during beam
Regulation
Be7 < 30Bq/cc
H3 < 42Bq/cc
New DP tank 240m3
New facility building

## Slide 25: Radio-active Air
Helium compressor
Helium compressor
Cooling water system
Cooling water system
Machine room
Service pit
Ground floor
Concrete shields
Storage area
Building
Chimney stack
Exhaust system
Radiation monitor
for exhaust air
Target
Horns
Helium vessel
Short-lifetime radio-activity like Ar41(t~2h) produced in underground area

## Slide 26: Radio-active Air
Helium compressor
Helium compressor
Cooling water system
Cooling water system
Machine room
Service pit
Ground floor
Concrete shields
Storage area
Building
Chimney stack
Regulation by law:
< 0.5 mBq/cc
Exhaust system
Radiation monitor
for exhaust air
Target
Horns
Go out through exhaust line
Leakage of radioactive air
from underground area
through gaps
Helium vessel

## Slide 27: Air Tightness Improvement
Caulking between concrete shields
Lay the air-tight sheet
Lay the protection sheet under air-tight sheet
Air-tight sheet
(made of the same material for balloon)
Protection sheet
(over air-tight sheet)

## Slide 28: Radio-active Air
Helium compressor
Helium compressor
Cooling water system
Cooling water system
Machine room
Service pit
Ground floor
Concrete shields
Storage area
Building
Chimney stack
Regulation by law:
< 0.5 mBq/cc
Caulking + Air-tight sheet
Exhaust system
Radiation monitor
for exhaust air
Target
Horns
Now :
~0.2 mBq/cc
@ 230kW
Go out through exhaust line
Leak rate reduced, but leakage happens
through the edge of sheet.
Helium vessel
Acceptable beam power
~500kW

## Slide 29: Radio-active Air
Helium compressor
Helium compressor
Cooling water system
Cooling water system
Machine room
Service pit
Ground floor
Concrete shields
Storage area
Building
Chimney stack
Regulation by law:
< 0.5 mBq/cc
Caulking + Air-tight sheet
Exhaust system
Radiation monitor
for exhaust air
Target
Horns
Go out through exhaust line
Helium vessel
Add air-tight lamination (made of steel and air-tight material) under concrete shields
Acceptable beam power > 1MW
(should be confirmed with actual setup)

## Slide 30: Acceptable Beam Power
Acceptance of each component for high power beam
  Target
    Mechanical: 0.75MW
    Cooling: 0.75MW
  Horn
    Cooling for conductors: 1.85MW
    Cooling for striplines: 0.4MW  0.75MW (2014~)
    Hydrogen production: 0.3MW  > 1MW (2014~)
    Power supply: 0.4Hz, 250kA  1Hz, 320kA (2014~)
  He vessel, Decay Volume & Beam Dump
    Cooling: 4MW(HV&DV), 3MW(BD)
  Facility
    Water disposal: 0.5MW  2MW (2016 or 2017~)
    Radio-active air: 0.5MW  > 1MW (2014~)
Graphite material is supposed to withstand up to ~1.5MW, when optimization of design including beam size, horn shape, cooling, etc is done.

## Slide 31: Summary
J-PARC neutrino beamline is designed for 750kW beam
J-PARC accelerator aims to achieve 750kW beam with 1Hz operation.
There are some devices which limit acceptable beam power.
Several upgrades are planed to accept 750kW beam.