## Slide 1: Neutrino Program in China
Jingyu Tang
Institute of High Energy Physics, CAS
ICFA Neutrino Panel – Asian Community Meeting
Nov.13, 2013, Kashiwa City, Chiba, Japan

## Slide 2: Outline
Introduction to neutrino experiments in China
  Present: Daya Bay Neutrino Experiment
Near future: Jiangmen Neutrino Experiment (JUNO)
Long term: MOMENT – a muon-decay medium baseline neutrino beam
Summary

## Slide 3: Introduction to Neutrino Experiments in China
China started the neutrino experiment program from 2003, with IHEP as the core and the driving engine
Became a very important part of high-energy physics in China
Three major steps:
  Daya Bay experiment (in operation)
  JUNO experiment (under construction)
  MOMENT experiment (planning, long term)
Uniting domestic researchers (universities and institutes) and attracting international collaboration

## Slide 4: Daya Bay Neutrino Experiment
First neutrino experiment facility
  Based on Daya Bay reactor
Milestones:
  2003: project proposed
  2006: project approved
  2007: ground breaking
  2011: installation completed, data taking started
  2012.3: announcing the discovery of new neutrino oscillation (13 measured to be non-zero)
  2013.8: announced the first direct measurement of
  and more precise measurement on 13
  Continue data taking for 4-5 years more

## Slide 5: Summary
Preliminary study of the neutrino beam MOMENT looks competitive
  Muon-decayed neutrinos (advantage in background)
  High neutrino flux with neutrino energy: 100-400 MeV
  Not a facility project yet, just concept study
Following studies will focus on
  Suitable detector and baseline distance
  Optimization of the target station (used protons, heat and radiation)
  Higher field (14 T) for the capture solenoid
  Optimization of transport/decay channels
Technical difficulties
  Proton driver: to be solved by China-ADS and others
  Target and very high field SC solenoids: collaboration and R&D
  Detector: to be identified

## Slide 6
Thank you for attention!

## Slide 7: Daya Bay Experiment
Completed all installations in Sep. 2012.
AD8
AD7
8 AD run
We are here
Uncertainty of sin2213

## Slide 8: JUNO Experiment
Daya Bay
Daya Bay II
20 kton LS detector
3%/E̅ resolution
Rich physics
  Mass hierarchy
  Precision measurement of 4 oscillation parameters to <1%
  Supernovae neutrino
  Geoneutrino
  Sterile neutrino
  Atmospheric neutrinos
  Exotic searches
Talk by Y.F. Wang at ICFA seminar 2008...NuFact 2012; by J. Cao at Nutel 2009...NPB 2012 (ShenZhen);
Paper by L. Zhan, Y.F. Wang, J. Cao, L.J. Wen, PRD78:111103,2008; PRD79:073007,2009
JUNO (DYB-II) has been approved in China in Feb. 2013
Equivalent to CD1 of US DOE

## Slide 9: The reactors and site
 | Daya Bay | Huizhou | Lufeng | Yangjiang | Taishan
Status | Operational | Planned | Planned | Under construction | Under construction
Power | 17.4 GW | 17.4 GW | 17.4 GW | 17.4 GW | 18.4 GW
Daya Bay
Huizhou
Lufeng
Yangjiang
Taishan
Hong Kong
Kaipin, Jiangmeng, Guang Dong
Scheduled data taking ~2020
Site survey and civil design:
34.5m

## Slide 10: Projected Sensitivity
Dashed lines: relative measurement determines the MH to 3 in 6 years.
Solid lines: with 1% precision m2μμ measurement from T2K and Nova, sensitivity increase to 4.
core distribution and energy non-linearity included.
 | DYB | JUNO
Dm212 | 3% | 0.6%
Dm223 | 5% | 0.6%
sin2q12 | 6% | 0.7%
sin2q23 | 20% | N/A
sin2q13 | 14% 4% | ~ 15%
Will be more precise than CKM matrix elements !
Probing the unitarity of UPMNS to ~1% level
arXiv:1303.6733

## Slide 11: JUNO Project Planning
Complete CDR
Start civil bidding
2013
2014
Start civil construction
PMT prototype
Build PMT production line
2015
2016
Complete TDR
Start PMT mass
production
Equipment bidding
Complete tunnel
Start detector
Installation
Ready for LS
production
2017
2018
Complete detector
installation
LS into tank
Complete install.
Testing
Start data taking
2019

## Slide 12: A dedicated facility for CP measurements?
  JUNO and other experiments
  Measurements in Mass Hierarchy and other mixed parameters
It looks that CP phase measurement will be the last undetermined key property of neutrino.
A good dedicated machine to measure CP phase

## Slide 13: MOMENT: A muon-decay medium baseline neutrino beam facility
A new idea on neutrino beam
Using a CW proton linac as the proton driver
  Simplified design from the China-ADS linac
  1.5 GeV, 10 mA  15 MW in beam power
  Mercury jet target in high-field SC solenoid
  Collection of pions and muons
Muon transport and decay channel
  Pure + or - decay
High neutrino flux at a detector of >50 km

## Slide 14: Schematic for MOMENT
Detector

## Slide 15: A 0-free neutrino beam line
Neutrino energy: ~ 300 MeV  baseline = 150 km
Although we loose some statistics due to the lower cross section, but we gain by being background free from p0

## Slide 16: Proton Driver
A CW proton SC linac can provide the highest beam power, and selected as the proton driver for MOMENT
China-ADS project was launched in beginning 2011, with a long-term goal to drive a subcritical reactor with 12-15 MW proton beam; MYRRHA is also developing a CW proton linac of lower power. And Project-X for CW RF but chopped beam.
One of the main goals in the China-ADS R&D phase is to develop the relevant technologies with the SC proton linac working in CW mode
If R&D successful in CW linac, in early 2020, the accumulated experience will allow us to build a proton driver based on the similar CW linac in GeV but with much lower requirement on reliability

## Slide 17: Design scheme for the proton driver
Design goal:
  Beam energy: 1.5 GeV
  Beam current: 10 mA
Simplified design scheme from the China-ADS design
  Much less redundancy wrt China-ADS
  3.2-MeV RFQ (room-temperature)
  Three sections SC spoke cavities (160 MeV)
  Two sections SC elliptical cavities (1.5 GeV)
  In total, 195 SC cavities in 52 cryostats, linac length: ~ 300 m

## Slide 18: Lattice of the linac
a: Spoke021 section, b: Spoke040 section, c: Ellip063 section,
d: Ellip082 section (<1 GeV), e: Ellip082 section (> 1 GeV)

## Slide 19: Higher proton energy?
Study shows that neutrino yield per proton is slightly more than proportional to beam energy
If beam power keeps unchanged, neutrino flux will increase slightly with increasing proton energy
  More benefit in the pion beam core
  Pion energy spectrum shifts towards higher
Anyway, alternative proton driver schemes with higher energy have also been studied.

## Slide 20: Target and pion/muon collection - Target
Mercury jet target (similar to NF design, MERIT experiment)
  Higher beam power: heat load, radioactivity
  On the other hand, easier to some extent due to CW proton beam (no shock-wave problem)
Other target solutions such as fluidized tungsten-powder target can also been considered

## Slide 21
Magnetic field of main SC solenoid: 10 T
Target: radius - 4 mm, effective length – 30 cm
Pion production ratio: 0.15 /p @1.5 GeV
Similar field configuration as at COMET
Chart: Magnetic Field Curve
14 T capture field is under study

## Slide 22: Large heat deposit and irradiation in SC solenoids
Pion energy spectrum at exit (4 m from target center)
0.8kW
0.15kW
0.06kW
0.05kW
In coils: 3.1 X 1015 n/m2/s

## Slide 23: Pion/muon collection and transport
A straight section in SC solenoids of about 50 m to match the SC solenoids at the target, and for the pions to decay into muons
  Adiabatic field transition from the high capture field to the lower focusing field to convert transverse momentum into longitudinal
  Chicane in the beginning to collect scattered protons
  Very large emittance and momentum spread
  Pions with lower energy decay faster
Similar beam rigidity assures that pions and muons can be transported in the same focusing channel
  Momentum and emittance of pions almost preserved in muons

## Slide 24: Collection and transport efficiency
  Modest acceptance for channels
  About 0.0052 +/proton for about 50 mm-rad at entrance of muon decay channel
  Emittance limitation is acceptable
Try to transport large momentum range /
Expected: >±50% centered at 300 MeV/c
 | muon/proton | Portion（%）
No limit on emittance | 9.48E-03 | 100
Emittance: 100 πmm-rad | 8.04E-03 | 85
Emittance: 80 πmm-rad | 7.31E-03 | 77
Emittance: 50 πmm-rad | 5.22E-03 | 55
Emittance limit in both (X-X’) and (Y-Y’)
7 T

## Slide 25
A selection section of about 2 m (length) to select +/+ from -/-, as either + beam or - beam is used for producing the required neutrinos
  For very large emittance, a group of three SC dipoles with strong gradient (similar as an DFD FFAG focusing) is used for bending (e.g., 40  /-80  /40 ) and focusing
  Reverse the fields when changing from + to -

## Slide 26: Muon transport and decay - Muon bending section
A bending section is required before the muon decay channel, to suppress the background of pion-decayed neutrinos at the detector by limiting the momentum acceptance when needed
  Bending angle is adaptable according to the general layout
  More energetic pions continue to decay in the section
Many short SC solenoids aligned with increased angle displacement to bend and focus the beam simultaneously
  Short solenoids helps reduce beam centroid excursion (aperture, beam loss)
  Alternate reverse SC field also helps reduce the excursion, and emittance coupling
  A small vertical field component is also helpful to reduce the excursion and for momentum selection

## Slide 27
Beam tracking simulated by G4beamline
Θ=2°
Field distribution (left) and beam centroid evolution (right)
Bending section by slanted solenoids (39*2=78) has very good momentum acceptance, p/p>50%
Small vertical component (~0.055 T) helps

## Slide 28: Muon transport and decay - Muon decay channel
A long decay channel of about 600 m is designed for production of neutrinos
  About 35% (centered momentum: ~300 MeV/c)
Important to have smaller divergent angle
  Neutrino energy spectrum at detector related to the angle
  Modest beam emittance and large aperture
  Adiabatic matching from 3.7 T in the bending section to 1.0 T in the decay section
Aperture/Field | Acceptance (mm-rad) X: in mm; X’: in mrad
600, 3.7 T | 100 (x: 280, x’: 357)
800, 1.0 T | 65 (x: 380, x’: 171)

## Slide 29: Neutrino energy spectra dependent on muon momentum and divergent angle

## Slide 30: Neutrino flux and possible detector
Suitable detector for MOMENT is still under study
  100-150 km from the target/source
  Mass: 0.1-1 Mton
  Simultaneous detection of all four neutrino types: ,
  Flavor sensitive, charge sensitive and NC/CC sensitive
  One example is Gd-doped water detector
Neutrino spectra at the detector centered at about 250 MeV
Energy spectra of decayed muons and neutrino at detector

## Slide 31: Estimate of neutrino flux
Proton on target ( operation 5000 h): 1.125  1024 proton/year
Muon yield: 1.62  10-2 /proton
Muon decay probability: 0.35
Total neutrino yield: 4.4  10-3 /proton (in pair)
5.0  1021 /year (in pair)
(NF: 1.1  1021 /year )
Neutrino flux at detector: dependent on the distance
4.6  1011 /m2/year (@150 km)

## Slide 32: Summary
China has well established a neutrino program into the future
Daya Bay will continue to produce good experiment results
JUNO will participate in the world competition for the measurement on mass hierarchy
MOMENT is still a concept, and a far way to go; it looks competitive in the CP violation measurement
Collaboration and competition with leading labs coexist at the same time, and are helpful for the neutrino community

## Slide 33
Thank you for attention!