## Slide 1: Simulation-based Inference for Precision Neutrino Physics through Neural Monte Carlo Tuning
Arsenii Gavrikov, Andrea Serafini, Dmitry Dolzhikov
on behalf of the JUNO Collaboration
University of Padova & INFN Padova, Italy andrea.serafini@pd.infn.it
Pre-print
Repo

## Slide 2: Simulation-based Inference for Precision Neutrino Physics through Neural Monte Carlo Tuning
Arsenii Gavrikov, Andrea Serafini, Dmitry Dolzhikov
on behalf of the JUNO Collaboration
University of Padova & INFN Padova, Italy andrea.serafini@pd.infn.it
Pre-print
Repo
Our ML guru
JUNO analysis fit/statistics enthusiasts

## Slide 3: The JUNO experiment
What is JUNO (Jiangmen Underground Neutrino Observatory)? [1]
Large-scale, next-generation liquid scintillator (LS) detector
It features a massive 20-kiloton LS target
Monitored by over 43,000 Photomultiplier Tubes (PMTs) to detect light
Primary Physics Goals [2, 3]
Determine the Neutrino Mass Ordering (NMO).
Measure three neutrino oscillation parameters (, ,) with sub-percent precision
Broad physics program including geoneutrinos, supernovae, and more
The Core Challenge
Unprecedented <3% @ 1 MeV energy resolution and <1% control over energy-scale systematic uncertainties
 need for on highly accurate and well-tuned Monte Carlo (MC) simulations!
[1] JUNO Collaboration 2016 J. Phys. G: Nucl. Part. Phys. 43 030401 [2] JUNO Collaboration 2022 Chinese Phys. C 46 123001 [3] JUNO Collaboration 2025 Chinese Phys. C 49 3, 033104
  Running since August 2025!!!

## Slide 4: The Energy Response Challenge
How JUNO Detects Events
JUNO is a calorimeter: a particle deposits energy in the scintillator.
The scintillator emits light collected by PMTs and measured as a total number of photo-electrons (NPE)  our proxy for the visible energy

## Slide 5: The Energy Response Challenge
How JUNO Detects Events
JUNO is a calorimeter: a particle deposits energy in the scintillator.
The scintillator emits light collected by PMTs and measured as a total number of photo-electrons (NPE)  our proxy for the visible energy
The Problem: A Non-Linear Response
The relationship between true deposited energy and NPE is not linear.
Non-linearity in the MC modeled by three key physical parameters:
  Birks' Coefficient () ↓: models quenching (energy lost as heat instead of light at high ionization) reducing the signal.
  Cherenkov Factor () ↑ : models the fraction of Cherenkov light produced by secondary particles absorbed and re-emitted.
  Light Yield () ↑: models the overall scaling factor for the number of scintillation photons emitted per unit energy (after quenching).

## Slide 6: The Energy Response Challenge
How JUNO Detects Events
JUNO is a calorimeter: a particle deposits energy in the scintillator.
The scintillator emits light collected by PMTs and measured as a total number of photo-electrons (NPE)  our proxy for the visible energy
The Problem: A Non-Linear Response
The relationship between true deposited energy and NPE is not linear.
Non-linearity in the MC modeled by three key physical parameters:
  Birks' Coefficient () ↓: models quenching (energy lost as heat instead of light at high ionization) reducing the signal.
  Cherenkov Factor () ↑ : models the fraction of Cherenkov light produced by secondary particles absorbed and re-emitted.
  Light Yield () ↑: models the overall scaling factor for the number of scintillation photons emitted per unit energy (after quenching).
  Our Task: tune (, , ) so that our MC matches real calibration data.
↓
↓
↓

## Slide 7: Monte Carlo tuning strategy
Results best fit
MC
JUNO
Fitter
Minuit
MCMC
Nested sampling
Likelihood
Calibration data
Simulated data
The most straightforward approach would be...

## Slide 8: Monte Carlo tuning strategy
Results best fit
MC
JUNO
Fitter
Minuit
MCMC
Nested sampling
Likelihood
Calibration data
Simulated data
At each step of the fit, we generate a lot of events with full MC to build spectra of the sources with the corresponding kBg fCg LYg
The most straightforward approach would be...
too impractical and slow! Can we replace it with a surrogate model?
Analytically intractable

## Slide 9: Monte Carlo tuning strategy
The most straightforward approach would be...
too impractical and slow! Can we replace it with a surrogate model?
Approximated with SBI
ML generated data
Training
Fast ML model to get spectra for
(able to interpolate in param space)
Results best fit
MC
JUNO
Fitter
Minuit
MCMC
Nested sampling
Likelihood
Calibration data
Neural Likelihood Estimation (NLE)

## Slide 10: Monte Carlo tuning strategy
The most straightforward approach would be...
too impractical and slow! Can we replace it with a surrogate model?
Approximated with SBI
ML generated data
Training
Fast ML model to get spectra for
(able to interpolate in param space)
Results best fit
MC
JUNO
Fitter
Minuit
MCMC
Nested sampling
Likelihood
Calibration data
Neural Posterior Estimation (NPE)
directly outputting the posterior for ,
WHY NOT?
We wanted to:
keep model under control
use std. inference techniques
eventually use NLE as spectra generator (MC surrogate)

## Slide 11: Two Neural Likelihood Estimators
[1] Vaswani A et al, arxiv: 1706.03762
Multi-output regressor
Aims to directly learn a mapping from the parameters and a source type to the histogram representing the spectra PDF
Provides PDF estimation by outputting a histogram
Conditions: kB, fC, LY + source type S
+ straight and reliable model - requires pre-defined binning
+ exact probability density function
+ no pre-defined binning
+ opens a possibility of an unbinned fit
Normalizing Flow-based model
Aims to learn the exact conditional probability of the energies* for a given set of parameters and a source type:
*represented by amount of light collected
We use Normalizing Flows-based model [2] to evaluate the exact conditional probability for the events and build the PDF
Provides the exact conditional PDF for any energy value:
We use a Transformer encoder-based model [1] as the density estimator (TEDE)
[2] R. J. Rezende et al, arxiv: 1505.05770
TEDE
NFDE

## Slide 12: Transformer Encoder-based Density Estimator (TEDE)
Multi-output regressor is based on the Transformer's [1] encoder :
A powerful architecture, well known for NLP and CV applications
Each condition (MC parameter or source type) is treated as a token
Regressor Head block to convert outputs to the spectra PDF with pre-defined binning (bin size of 20 PEs)
[1] Vaswani A et al, arxiv: 1706.03762

## Slide 13: Normalizing Flows-based Density Estimator (NFDE)
[1] R. J. Rezende et al, arxiv: 1505.05770
Normalizing flows [1]:
generative ML model aimed to explicitly model a density estimation
generalizable for modeling a conditional density estimation as well
based on an idea of transforming a simple known distribution (e.g. standard Gaussian) to the complex, desired distribution by applying multiple learnable (using data) and invertible transformations called flows.

## Slide 14: Normalizing Flows-based Density Estimator (NFDE)
[1] R. J. Rezende et al, arxiv: 1505.05770
Normalizing flows [1]:
generative ML model aimed to explicitly model a density estimation
generalizable for modeling a conditional density estimation as well
based on an idea of transforming a simple known distribution (e.g. standard Gaussian) to the complex, desired distribution by applying multiple learnable (using data) and invertible transformations called flows.

## Slide 15: Normalizing Flows-based Density Estimator (NFDE)
[1] R. J. Rezende et al, arxiv: 1505.05770
Normalizing flows [1]:
generative ML model aimed to explicitly model a density estimation
generalizable for modeling a conditional density estimation as well
based on an idea of transforming a simple known distribution (e.g. standard Gaussian) to the complex, desired distribution by applying multiple learnable (using data) and invertible transformations called flows.
“Normalizing” direction
“Generative” direction

## Slide 16: Datasets: training/validation strategy
Y and kB example
Training data
21 points per param (213 combs)
10k events x 5 sources per point (~500M events)

## Slide 17: Datasets: training/validation strategy
Y and kB example
Training data
21 points per param (213 combs)
10k events x 5 sources per point (~500M events)

## Slide 18: Datasets: training/validation strategy
Y and kB example
Training data
21 points per param (213 combs)
10k events x 5 sources per point (~500M events)
Validation data #1
10 points per param (103 combs)
10k x 5 events per point (50M events)
 cover most of parameter space

## Slide 19: Datasets: training/validation strategy
Y and kB example
Training data
21 points per param (213 combs)
10k events x 5 sources per point (~500M events)
Validation data #1
10 points per param (103 combs)
10k x 5 events per point (50M events)
 cover most of parameter space
Validation data #2
3 points in total
10M x 5 events per point (150M events)
anchor PDF to high-stat spectra

## Slide 20: Datasets: training/validation strategy
Y and kB example
Training data
21 points per param (213 combs)
10k events x 5 sources per point (~500M events)
Validation data #1
10 points per param (103 combs)
10k x 5 events per point (50M events)
 cover most of parameter space
Validation data #2
3 points in total
10M x 5 events per point (150M events)
anchor PDF to high-stat spectra

## Slide 21: Datasets: training/validation strategy
Y and kB example
Training data
21 points per param (213 combs)
10k events x 5 sources per point (~500M events)
Validation data #1
10 points per param (103 combs)
10k x 5 events per point (50M events)
 cover most of parameter space
Validation data #2
3 points in total
10M x 5 events per point (150M events)
anchor PDF to high-stat spectra
Testing data #1
10 points per param (103 combs)
10k x 5 events per point (50M events)
 check possible biases over parameter space

## Slide 22: Datasets: training/validation strategy
Y and kB example
Training data
21 points per param (213 combs)
10k events x 5 sources per point (~500M events)
Validation data #1
10 points per param (103 combs)
10k x 5 events per point (50M events)
 cover most of parameter space
Validation data #2
3 points in total
10M x 5 events per point (150M events)
anchor PDF to high-stat spectra
Testing data #1
10 points per param (103 combs)
10k x 5 events per point (50M events)
 check possible biases over parameter space
Testing data #2
1 point
1000 x [1k; 2k; 5k; 10k; 25k] events x 5 with diff. seeds
 Analysis of systematic uncertainty of the model

## Slide 23: Datasets: training/validation strategy
Y and kB example
Training data
21 points per param (213 combs)
10k events x 5 sources per point (~500M events)
Validation data #1
10 points per param (103 combs)
10k x 5 events per point (50M events)
 cover most of parameter space
Validation data #2
3 points in total
10M x 5 events per point (150M events)
anchor PDF to high-stat spectra
Testing data #1
10 points per param (103 combs)
10k x 5 events per point (50M events)
 check possible biases over parameter space
Testing data #2
1 point
1000 x [1k; 2k; 5k; 10k; 25k] events x 5 with diff. seeds
 Analysis of systematic uncertainty of the model
1k events
25k events

## Slide 24: Datasets: training/validation strategy
Y and kB example
Training data
21 points per param (213 combs)
10k events x 5 sources per point (~500M events)
Validation data #1
10 points per param (103 combs)
10k x 5 events per point (50M events)
 cover most of parameter space
Validation data #2
3 points in total
10M x 5 events per point (150M events)
anchor PDF to high-stat spectra
Testing data #1
10 points per param (103 combs)
10k x 5 events per point (50M events)
 check possible biases over parameter space
Testing data #2
1 point
1000 x [1k; 2k; 5k; 10k; 25k] events x 5 with diff. seeds
 Analysis of systematic uncertainty of the model

## Slide 25: Training and validation of the models
For both models we use Kullback–Leibler divergence as the loss function for training:
As validation metrics we use p-norm distances between distributions' CDFs:
  as it is applicable for both TEDE and NFDE cases
p = 1: Wasserstein distance
p = 2: Cramer-von Mises distance
p = ∞: Kolmogorov-Smirnov distance

## Slide 26: Training and validation of the models
For both models we use Kullback–Leibler divergence as the loss function for training:
As validation metrics we use p-norm distances* between distributions' CDFs:
  as it is applicable for both TEDE and NFDE cases
p = 1: Wasserstein distance
p = 2: Cramer von Mises distance
p = ∞: Kolmogorov-Smirnov distance

## Slide 27: Parameter estimation
Example with NFDE:
Combined fit on all sources together
Cost function: Extended unbinned likelihood
Optimizer: Nested Sampling (ultranest)*
 Estimate the kB, fC, LY best parameters
 Explores full phase space, provides full posterior
 Shows correlations between the parameters
9.6
10.5
0.200
0.250
11600
11800
11700
0.225
10.05
kB
fC
LY
the testing dataset №1 point is between the points from the training dataset: interpolation
training points
*all fits performed with Minuit, MCMC (emcee), Nested Sampling (ultranest)  consistent results

## Slide 28: Parameter estimation
*all fits performed with Minuit, MCMC (emcee), Nested Sampling (ultranest)  consistent results
Model interpolation smooth and denoised
Model provides spctra estimates for any continuous values of the parameters​
9.6
10.5
0.200
0.250
11600
11800
11700
0.225
10.05
kB
fC
LY
Example with NFDE:
Combined fit on all sources together
Cost function: Extended unbinned likelihood
Optimizer: Nested Sampling (ultranest)*
 Estimate the kB, fC, LY best parameters
 Explores full phase space, provides full posterior
 Shows correlations between the parameters

## Slide 29: Parameter estimation
Example with NFDE:
Combined fit on all sources together
Cost function: Extended unbinned likelihood
Optimizer: Nested Sampling (ultranest)*
 Estimate the kB, fC, LY best parameters
 Explores full phase space, provides full posterior
 Shows correlations between the parameters
*all fits performed with Minuit, MCMC (emcee), Nested Sampling (ultranest)  consistent results
Parameters estimation combined:
kB: 10.13 +- 0.26 10.05 [g/cm2/GeV]
fC: 0.238 +- 0.029 0.225
LY: 11701 +- 23 11700 [1/MeV]
 well within 1σ (fluctuations expected for 1 fit)

## Slide 30: Learned dependences
PDF vs. parameter (almost linear)
PDFs vs. energy (NPE) (energy non-linearity)

## Slide 31: Evaluate ML-driven systematic uncertainty
uncertainties estimated by the fit can be compared with the actual variability of the best fit values
To perform systematic uncertainty estimation analysis, we use the testing dataset 2:
  Unseen during training point in the parameter space: kB, fC, LY = (15.45, 0.525, 10100)
  5 different exposures: 1k, 2k, 5k, 10k, 25k events
  1000 datasets with different MC generator seed per each exposure

## Slide 32: Estimation of ML-driven systematic uncertainty
To perform systematic uncertainty estimation analysis, we use the testing dataset 2:
  Unseen during training point in the parameter space: kB, fC, LY = (15.45, 0.525, 10100)
  5 different exposures: 1k, 2k, 5k, 10k, 25k events
  1000 datasets with different MC generator seed per each exposure
   Estimated uncertainty matches observed variability
Estimated Stat. Unc.
Observed Std. Dev.

## Slide 33: Estimation of ML-driven systematic bias
Using the testing dataset 1, one can check the bias across different points:
  Run MCMC fits per each testing point of the dataset
  Compare bias with the uncertainty obtained by the previous analysis for the 10k exposure point
   Observed biases are well within the uncertainty
Observed bias
Stat unc.

## Slide 34: Summary
  Challenge: systematics investigation for precision neutrino physics with JUNO and accurate energy calibration  requires an extremely well tuned MC, but the traditional MC tuning process is computationally prohibitive.

## Slide 35: Summary
  Challenge: systematics investigation for precision neutrino physics with JUNO and accurate energy calibration  requires an extremely well tuned MC, but the traditional MC tuning process is computationally prohibitive.
  Solution: we developed a Simulation-Based Inference framework using two neural likelihood estimators (TEDE and NFDE) that replace the slow MC simulation with a fast, accurate surrogate models.

## Slide 36: Summary
  Challenge: systematics investigation for precision neutrino physics with JUNO and accurate energy calibration  requires an extremely well tuned MC, but the traditional MC tuning process is computationally prohibitive.
  Solution: we developed a Simulation-Based Inference framework using two neural likelihood estimators (TEDE and NFDE) that replace the slow MC simulation with a fast, accurate surrogate models.
  Key Achievements:
  our models successfully learn the complex, non-linear energy response of the JUNO detector MC, including the strong correlations between , and parameters in the MC.
  when integrated with Bayesian inference, our method recovers all parameters with near-zero systematic bias.
  parameter uncertainties are limited purely by statistics and scale correctly as 1/ √N  possible to achieve <1% systematics
  This provides a flexible (binned or unbinned) framework for MC tuning with data! 

## Slide 37: Thanks!
Pre-print
Repo

## Slide 38: TEDE vs. NFDE (uncertainty)

## Slide 39: TEDE vs. NFDE (bias)

## Slide 40: Hyperparameters optimization

## Slide 41
How LS parameters impact the calibration data
Light yield is the most influential parameter​
All sources are highly affected
kB and fC are fixed:
  kB = 15.45 [g/cm2/GeV]
  fC = 0.525
LY is varying
Cs137
K40
Co60
Am-Be
Am-C
Only main peaks are shown
LY effect
Arsenii Gavrikov, Andrea Serafini, et al – NeuroMCT

## Slide 42
kB effect is smaller than LY and anticorrelated with the photo peak
All sources are affected
LY and fC are fixed:
  LY = 10100 [1/MeV]
  fC = 0.525
kB is varying
Cs137
K40
Co60
Am-Be
Am-C
Only main peaks are shown
How LS parameters impact the calibration data
kB effect
Arsenii Gavrikov, Andrea Serafini, et al – NeuroMCT

## Slide 43
fC has a minor effect to the spectra
Cs137 is not affected at all
Slight effect for Co60 and K40
kB and LY are fixed:
  kB = 15.45 [g/cm2/GeV]
  LY = 10100 [1/MeV]
fC is varying
Cs137
K40
Co60
Am-Be
Am-C
Only main peaks are shown
How LS parameters impact the calibration data
fC effect
Arsenii Gavrikov, Andrea Serafini, et al – NeuroMCT

## Slide 44: The JUNO detection process
JUNO will measure the antineutrinos () generated in the fissions occurring in 8 nuclear cores at 52.5 km
The detection is based on a charged current interaction named Inverse Beta Decay (IBD) on protons (p)
 sensitive only to electron
Detection relies on a double coincidence:
prompt signal: positron (e+) annihilation
delayed signal: neutron (n) capture
 strong handle against most backgrounds

## Slide 45: The JUNO detector
35.4 m
43.5 m
 | Target mass [kton] | Energy resolution | Light yield [PE/MeV]
Daya Bay | 0.02 | 8%/√E | 160
Borexino | 0.3 | 5%/√E | 500
KamLAND | 1 | 6%/√E | 250
JUNO | 20 | 3%/√E | ~1600
Main requirements:
high statistics  20 kton of liquid scintillator acrylic sphere
<3% energy resolution @ 1 MeV  photocoverage ~78%
energy-scale systematics below 1%  17612 20" Large-PMT  25600 3" Small-PMT
[Prog. Part. Nucl. Phys. 2021.103927]

## Slide 46: Detector response: what JUNO actually sees
interaction
light emission
light detection
Antineutrino energy
Deposited energy
Visible energy
Reconstructed energy
Calibration campaigns
automated multiple-position and multi-source calibration (link)
periodic calibration campaigns
dual-calorimetry system (link)
Energy resolution
Stochastic term: light yield (from source calibration)
Dominated by non-uniformity
(from multi-source calibration)
PMT dark noise
Energy [MeV]
Events/bin [#/20 keV]
Events/bin [#/20 keV]
Deposited energy [MeV]
Events/bin [#/20 keV]
Visible energy [MeV]
Energy resol. [%]
Visible/deposited
Deposited spectrum
Visible spectrum
Reconstructed spectrum
Non-linearity
6 years

## Slide 47: Detector response: what JUNO actually sees
interaction
light emission
light detection
Antineutrino energy
Deposited energy
Visible energy
Reconstructed energy
Calibration campaigns
automated multiple-position and multi-source calibration (link)
periodic calibration campaigns
dual-calorimetry system (link)
Energy resolution
Stochastic term: light yield (from source calibration)
Dominated by non-uniformity
(from multi-source calibration)
PMT dark noise

## Slide 48: JUNO detector response: state of the art
Updated values based on commissioning data and realistic MC simulation
Realistic MC simulation
Measured data

## Slide 49: IBD backgrounds in JUNO
JUNO employs various selection cuts to retain high efficiency and assure high purity in the IBD signal:
Cosmogenic backgrounds  muon veto
Accidental coincidences  fiducial volume + IBD cuts
Irreducible backgrounds  negligible (~1/20 of signal)
IBD selection cuts | Efficiency [%] | IBD rate [day-1]
All IBDs | 100.0 | 57.4
Fiducial volume | 91.5 | 52.5
IBD selection | 98.1 | 51.1
Energy range | 99.8 | -
Time correlation (∆Tp-d) | 99.0 | -
Spatial correlation (∆Rp-d) | 99.2 | -
Muon veto (Time+spatial) | 91.6 | 47.1
Combined selection | 82.2 | 47.1
Residual backgrounds | Rate [day-1] | Rate unc. [%] | Shape unc. [%]
Geoneutrinos | 1.2 | 30 | 5
World reactors | 1.0 | 2 | 5
Accidentals | 0.8 | 1 | negligible
9Li/8He | 0.8 | 20 | 10
Atmospheric neutrinos | 0.16 | 50 | 50
Fast neutrons | 0.1 | 100 | 20
13C(α,n)16O | 0.05 | 50 | 50
Total background | 4.11 | - | -

## Slide 50: Detection channels in JUNO
CC on proton
NC on proton
CC on Carbon
NC on electron
Liquid scintillator:
Linear alkylbenzenes
C – 88%
H – 12%
NC recoil threshold: 200 keV

## Slide 51: Photomultiplier Tubes

## Slide 52: Dual calorimetry system
JUNO employs the dual calorimetry system to correct for electronics non-linearity
Sources of non-linear response:
Non-uniformity (NU)
Liquid scintillator non-linearity (LSNL)
Charge non-linearity (QNL) of L-PMTs
Simulations with extreme channel-level non-linearity of 50% over 100 PE show that L-PMT response () non-linearity can be corrected using S-PMT as calibration reference:
True electron energy [MeV]
Instrumental non-linearity
0
2
4
6
8
1.00
0.99
0.98
1.01

## Slide 53: Other non-linearities
Detector non-uniformity
The detector response to the same charge deposition depends on the position at which the event occurs and needs to be properly characterized.
Liquid scintillator non-linearity
Light emission has an intrinsic non-linearity because of:
Birks’ quenching effect in scintillation photon yield;
Velocity-dependent Cherenkov emission.
Non-linearity (visible/true)
0.98
1.04
1.00
True gamma energy [MeV]
1
2
3
4
5
6
0
0.96
0.92
0.94
0.90
1.02
Light Yield [PE/MeV]
1300
1600
1400
Radius [m]
0
2
4
6
8
1200
10
12
14
16
18
1500
Light yield @ center 1345 MeV  1665 MeV (new resolution model)

## Slide 54: Calibration of the JUNO detector
Radioactive sources (100-200 Hz) + Laser sources
1D: Automatic Calibration Unit (ACU)
2D: Cable Loop System (CLS)
3D: Remotely Operated under-LS Vehicles (ROV)
Boundary: Guide Tube Calibration System (GTCS)
Slide credits D. Basilico
250 calibration points
JHEP 03 (2021) 004

## Slide 55: Calibration strategy
Comprehensive calibration (250 points, ~48h)
basic understanding of the CD performance
Monthly calibrations (~100 points, ~11h)
monitor non-uniformity
Weekly calibrations (~15 points, ~2.4h)
track variations in LY of LS, PMT gains, and electronics
Slide credits D. Basilico
JHEP 03 (2021) 004

## Slide 56
Normalizing flows-based density estimation
[1] R. J. Rezende et al, arxiv: 1505.05770
x: input data
Arsenii Gavrikov, Andrea Serafini, et al – NeuroMCT
8.1
"Normalizing" direction
"Generative" direction
Normalizing flows [1]:
  Generative machine learning model
  Aims to explicitly model a density estimation
  Can be generalized for modeling a conditional density estimation as well
  To obtain a value from the target distribution:
    sample a value from the base distribution and passing it through all the flows

## Slide 57
Normalizing flows-based density estimation
Normalizing flows are based on an idea of transforming a simple known distribution (e.g. standard Gaussian) to the complex, desired distribution by applying multiple learnable (using data) transformations
Each transformation is called Flow and must be invertible
[1] R. J. Rezende et al, arxiv: 1505.05770
x: input data
Arsenii Gavrikov, Andrea Serafini, et al – NeuroMCT
8.2
Normalizing flows [1]:
  Generative machine learning model
  Aims to explicitly model a density estimation
  Can be generalized for modeling a conditional density estimation as well
  To obtain a value from the target distribution:
    sample a value from the base distribution and passing it through all the flows
"Normalizing" direction
"Generative" direction

## Slide 58
Normalizing flows-based density estimation
x: input data
[1] R. J. Rezende et al, arxiv: 1505.05770
Arsenii Gavrikov, Andrea Serafini, et al – NeuroMCT
8.3
"Normalizing" direction
"Generative" direction
Normalizing flows [1]:
  Transformations can be very diverse as long as they follow the invertibility condition
  We use Planar flow:

## Slide 59
Normalizing flows-based density estimation
Normalizing flows [1]:
  Transformations can be very diverse as long as they follow the invertibility condition
  We use Planar flow:
    where parameters are parametrized by neural networks to include the conditions (MC parameters + source type): conditional probability
x: input data
Arsenii Gavrikov, Andrea Serafini, et al – NeuroMCT
8.4
"Normalizing" direction
"Generative" direction
[1] R. J. Rezende et al, arxiv: 1505.05770

## Slide 60
Normalizing flows [1]:
  Transformations can be very diverse as long as they follow the invertibility condition
  We use Planar flow:
    where parameters are parametrized by neural networks to include the conditions (MC parameters + source type): conditional probability
How to perform the inference with the model?
Normalizing flows-based density estimation
x: input data
[1] R. J. Rezende et al, arxiv: 1505.05770
Arsenii Gavrikov, Andrea Serafini, et al – NeuroMCT
8.5
"Normalizing" direction
"Generative" direction

## Slide 61
Normalizing flows [1]:
  Transformations can be very diverse as long as they follow the invertibility condition
  We use Planar flow:
    where parameters are parametrized by neural networks to include the conditions (MC parameters + source type): conditional probability
How to perform the inference with the model?
Normalizing flows-based density estimation
x: input data
[1] R. J. Rezende et al, arxiv: 1505.05770
Arsenii Gavrikov, Andrea Serafini, et al – NeuroMCT
8.6
"Normalizing" direction
"Generative" direction
MC parameters + source type
Data
well-known (e.g. standard Gaussian)
Computed based on the learned transformations