## Slide 1: Borexino Detector Calibration System
Szymon Manecki, VirginaTech

## Slide 2: Virginia Tech

## Slide 3: Virginia Tech
Center for Neutrino Physics

## Slide 4: Virginia Tech
Center for Neutrino Physics
Faculty (with focus on neutrinos)
  Bruce Vogelaar
  Jon Link
  Camillo Mariani
Important Events
  “International Neutrino Summer School” (2012)
  “Sterile Neutrinos at the Crossroads” (2011 workshop)
  Center for Neutrino Physics (established 2011)
Principle Topics
  Borexino (since inception)
  LENS (since inception)
  Daya Bay
  MiniBooNE
  Double Chooz
  LBNE
Tatsu Takeuchi (theory)
  Patrick Huber (theory)
Raju Raghavan (th. exp.) (recently deceased: Oct 2011)
VT Neutrino Funding
  NSF (1999) $5.8M
  DOE (2006) $2.0M

## Slide 5: Virginia Tech
mini-LENS (Low Energy Neutrino Spectroscopy)
Neutron Spectrometer
 Decay to Excited States
HPGe Low-Bkgd Screening
MALBEK (Majorana 0)
39Ar Depleted Argon
Office
A
B
C
D
E
F
G
Kimballton Underground Research Facility
1400 m.w.e.

## Slide 6
3 ns rise time
3 ns FWHM
Light Pulse as Viewed by a PMT
Daya Bay µ Veto
Jon Link and his team was responsible for the Water Pool calibration System
  Relative timing of all PMTs;
  Monitoring water quality;
  Monitor PMT gains;
  150 LED flashers;
  Teflon diffuser balls optimally distributed giving uniform light to all the PMTs;

## Slide 7: Borexino Detector

## Slide 8: Borexino Detector
Design
Graded Shielding
Real-time Spectroscopy
2214 PMTs
Ultra-pure Target
PC + PPO (238U / 232Th ~ 10-18 g/g)
Neutrino Physics via
Electron Elastic Scattering
Resolution at 1 MeV:
5% [energy]; ~ 10-15cm [position]
Muon rejection: Efficiency > 99.992%

## Slide 9: Major Publications
Pep & CNO limit : Phys. Rev. Lett. 108 (2012) 051302.
7Be Adn: Physics Letters B 707 (2012) 22-26.
7Be @ 5%: Phys. Rev. Lett. 107 (2011) 141302.
8B > 3 MeV: Phys. Rev. D 82 (2010) 033006.
Solar antinu limits: Phys. Lett. B 696 (2011) 191-196.
7Be @ 10%: Phys. Rev. Lett. 101 (2008) 091302.
7Be @ 17%: C. Arpesella at al. (Borexino collaboration):

## Slide 10: Detector Calibration

## Slide 11: Detector Calibration
• Determination of the energy scale;
• Study of the uniformity of the detector response;
• Study of FV systematics at different energies and for different FV cuts;
• Validation of the Borexino Monte Carlo code and of the analytical models that are used in the analysis to describe the detector response;
• Study of the detector trigger efficiency regarding 14C and 85Kr bkg;
• The purity of the scintillator;
• Determination of the source
source position better than 2 cm;
• Spectral shapes must represent the internal backgrounds;
• Cost, simplicity and performance
combined with versatility of the
calibration sources (alpha, beta,
gamma, laser etc.);
• The access pipe only 10 cm in diameter;
Goals Constrains

## Slide 12: Hardware System
Source Location and Insertion
• 7 consumer-grade Kodak cameras;
• PMT positions used as reference pnt;
• Source position determined with
an additional LED;
• 1-m neutrally buoyant rods;
• Operated in Class-10 glove-box;
• 95% of the detector volume
covered;

## Slide 13: Hardware System
Source Location and Insertion

## Slide 14: Source Insertion System
  • One rod has a hinge in the center; Spring-mounted source is at the end;
  • Teflon tube containing fiber optic is used to pull assembly off axis;
  • 6-way cross couples gate valve to glovebox;
  • Sliding seals for rod and tether maintain cross-glovebox ∆q;
  Computer controlled process system:
  • Maintains N2 pressure & flow
  • Monitors O2 and liquid levels

## Slide 15: Source Location System
  • Remote controlled
  • Fitted with separate fish-eye lens
  • Halogen bulbs for illumination
  • Known PMT positions for self-calibration
  • Pinhole LEDs used to account for scale + offset in subsequent images
  • Searches red pixels in each image for “bright spot”
  • Discard cameras with > 2 cm distance from fit position (min 2 CCDs required)

## Slide 16: Calibration Campaigns
Type | γ |  |  |  |  |  |  |  | β |  | α | n |  | 
Src. | 57Co | 139Ce | 203Hg | 85Sr | 54Mn | 65Zn | 60Co | 40K | 14C | 214Bi | 214Po | n-p | n-12C | n-Fe
MeV | 0.122 | 0.165 | 0.279 | 0.514 | 0.834 | 1.1 | 1.1, 1.3 | 1.4 | 0.15 | 3.2 | 7.69 (0.84) | 2.23 | 4.94 | ~7.5
  • 4 campaigns Oct ’08, Jan ’09, Jun ’09, Jul ’09;
  • 12 different sources;
  • 295 different locations;
  • 54 days with 65 % duty cycle;

## Slide 17: Calibration Results
Energy Scale
β
α
β- events
and
α- events
Pulse Shape
Position
Quenching
Gatti Parameter
•

## Slide 18: Calibration Results
Systematics |  | 
Livetime | 0.1% | 0.04%
Scintillator ρ | 0.2% | 0.05%
Event Selection Loss | 0.3% | 0.1%
Position Reconstruction | 6.0% | +1.3%/-0.5%
Energy Scale | 6.0% | 2.7%
TOTAL | 8.5% | +3.6%/ -3.4%
• Room for improvement:
Position Reconstruction + 1.3, -0.5 %
Energy Scale ± 2.7%
• The system can be used at any point:
Required manpower – 30 members (full campaign)
Short campaigns also considered (Radon, laser sources)
Original goal ± 2 cm
± 0.6 cm

## Slide 19: Conclusions
• Calibration software and hardware developed and built at Virginia Tech;
• System was used in multiple campaigns and proved to be highly reliable;
• For Borexino, radiopurity in the region of interest was of major concern
but no long-term contamination due to calibrations has been identified;
• Systematic errors in Borexino were reduced by more than a factor of 2;
• Large operational range allowed to study the energy reconstruction uniformity;
• The system remains on site, ready for immediate implementation;
Currently awaiting the end of data-taking phase II in Borexino .

## Slide 21: Backup

## Slide 22: Position Reco
Chart: 
Mechanical Ruler Check